## Slide 1: MFMC GBAS – Flight Trials and Performance Studies
ENC 2016 – Helsinki – 01.06.2016
M. Felux, M.-S. Circiu, D. Gerbeth
Daniel.Gerbeth@dlr.de

## Slide 2: Multi-Frequency Multi-Constellation GBAS Why? How?
Protection against ionospheric gradient threat
Ionospheric scintillation issues in high/low latitudes
Weak constellations and required masking may have impact on performance

## Slide 3: Motivation Why?
Large ionospheric gradients and scintillation events can result in
significant unavailability of the GBAS
Graphic from: Hlubek N, Berdermann J, Wilken V, Gewies S, Jakowski N, et al.: Scintillations of the GPS, GLONASS, and
Galileo signals at equatorial latitude. J. Space Weather Space Clim., 2014, 4, A22
Notes: Iono gradients – scintillations
Next: Motivation overview

## Slide 4: Motivation How?
Dual-frequency GBAS can tackle the ionospheric gradient problem
Multi constellation GBAS can reduce the impact of scintillations on availability
Quickly growing Galileo constellation (all satellites with E1/E5a)
Currently 12 GPS Block IIF satellites with L1 and L5 operational, continuous launches all with second frequency
Notes: Next: Outline

## Slide 5: L5/E5a Satellite Status (12 GPS Block IIF, 14 (9) Galileo)
GPS Block IIF and Galileo status

## Slide 6: Performance Metric: Availability
Represented by protection levels:
Need to determine all the necessary parameters for the processing modes
Analysis of extesive ground and flight data to establish expectable performance models

## Slide 7: Data Collection
Airbus A320
Dornier DO-228
Antenna: Antcom multiband
Duration: 100 hours A320 since May 2015 6 hours Dornier March 2015
Receiver: Javad Delta
23 Mhz bandwidth
2 correlator spacings

## Slide 8: Towards MFMC GBAS – Performance Assessments Sigmaair
Elevation in A/C body frame [deg]

## Slide 9: DLR Ground Facility Braunschweig Airport
 | L1 | L2 | L5
BR01 |  |  | 
BR02 |  |  | 
BR03 |  |  | 
BR05 |  |  | 
Javad Delta Receivers with
GPS (L1/L2/L5) + Galileo (E1/E5a) + Glonass + BDS
Connected to Leica AR25 choke ring antennas

## Slide 10: Evaluating Performance of GPS L5 and Galileo E1/E5a Using Ground Measurements
Improved performance of the Galileo signals
RX configuration:
  0.1 chips correlator spacing (L1/E1)
  1 chip correlator spacing (L5/E5a)
Multipath and noise on Galileo E1 is lower than on GPS L1, especially at low elevation
  BOC(1,1) modulation
  Wider transmission bandwidth
Galileo E5a shows lower multipath and noise than Galileo E1
  BPSK(10) signal
  Higher chip rate
  Higher signal power
Paper presented at ITM 2015 : M-S Circiu et. Al – “Evaluation of GPS L5, Galileo E1 and Galileo E5a Performance for Multi Frequency Multi Constellation GBAS”
10 GPS Block IIF , 4 Galileo
40 days of data – 100 sec smoothing constant

## Slide 11: Dual-Frequency Dual-Constellation GBAS Flight Trials
4 flights in March 2015 with Dornier DO-228 (6h total)
Satellite visibility: 5-7 dual frequency (GPS+Gal)
Single-frequency L5/E5a GPS and Galileo
Dual-frequency L1/E1+L5/E5a GPS and Galileo

## Slide 12: Protection Levels Contribution of Different Sigma Terms
GPS L1 30s (GAST D)
GPS L5 30s

## Slide 13: Protection Levels Contribution of Different Sigma Terms
GPS L1 30s (GAST D)
GPS L1/L5 100s Ifree

## Slide 14: Comparison and Trade-Off Studies 30s Smoothing Constant
‘Nominal Performance of Future Dual-Frequency Dual-Constellation GBAS’ In press, August 2016, IJAE

## Slide 15: Comparison and Trade-Off Studies 100s Smoothing Constant
‘Nominal Performance of Future Dual-Frequency Dual-Constellation GBAS’ In press, August 2016, IJAE

## Slide 16: Conclusions
Dual frequency and multi constellation GBAS can resolve many of the current GBAS issues
More data and investigations needed for suitable models covering all aircraft, receivers, antennas etc.
No solution to all problems
No defined way ahead concerning different modes
Trade-off is a difficult task

## Slide 17: Thank you for your attention! Questions?