## Slide 1: Effectiveness of [...] INCENTIVES on EV-uptake considering [...] frameworks within the EU
Christoph Schimeczek, Doruk Özdemir, Stephan Schmid
German Aerospace Center (DLR) Institute of Vehicle Concepts
@ ETC Barcelona, October 6th 2016

## Slide 2: The challenges
Which incentives are most effective?
Which user group will profit?
Electric Vehicles (EV)
Traffic
CO2 emissions
noise
air pollution
Provide incentives
EV uptake
charging time
electric range
purchase cost
Incentives
different incentives
varying effects

## Slide 3: Approach
national boundary conditions
TCO
+
vehicle utility
effective-ness of incentives
fleet types & vehicle usage
private & corporate ownership
4 years of ownership
Netherlands
Austria
Germany
Spain
United Kingdom

## Slide 4: Fleet types
Annual mileages: 5,000 km/a ... 40,000 km/a
rented to vehicle users
purchased and maintained by rental company
car rental
purchased and owned by a single user
private ownership
allocated to a single user
private and business purposes
company car
not allocated to a single person
used only on business purposes
commercial
Vehicle usage

## Slide 5: Boundary condition analysis
 | VAT | CV purchase tax (€) | BEV incentives (€) 1 | electricity cost (€/kWh) // diesel cost (€/l) 1 | company profit tax rate | employee income tax rate
DE | 19% | - | 4,000 | 0.33 // 1.15 | 30% | 52%
NL | 21% | 200 - 4,500 | - | 0.24 // 1.19 | 25% | 42%
AT | 20% | 1,500 - 7,000 | - | 0.23 // 1.08 | 25% | 43%
ES | 21% | 0 - 2,500 | 5,500 | 0.25 // 1.07 | 25% | 37%
UK | 20% | - | 6,500 | 0.23 // 1.49 | 23% | 40%
DE – high electricity prices, low fuel prices
AT & UK – high energy savings potential
Boundary conditions seem to favour Spain, Austria, UK.
No purchase taxes in DE & UK
No direct incentives in NL & AT
[1]1 £ = 1.3€

## Slide 6: Boundary conditions – Annual motor vehicle tax
Behold, it is log scaled!
significant differences between countries
good tax savings potential in NL & AT
G: gasoline
D: diesel
E: battery electric

## Slide 7: TCO – included items
TCO
purchase taxes
purchase incentives
registration cost
list price (+VAT)
motor tax
insurance cost
energy cost
maintenance & repair
company tax reliefs
cost of vehicle substitution
cost of money
resale value

## Slide 8: TCO – Vehicle substitution cost
real-world electric range
incidence of high daily mileage2
vehicle rental cost 3
BEVs drawbacks
  restricted range
  charging duration
1 P. Mock et al., „From laboratory to road - A 2015 update of official and “real-world” fuel consumption and CO2 values for passenger cars in Europe“, ICCT, White Paper, 2015.
2 DLR und Infas, „Mobilität in Deutschland 2008“, Ministerium für Verkehr, Bau und Stadtentwicklung, Bonn and Berlin, 2010.
3 www.billiger-mietwagen.de
Assumption
BEVs are replaced with conventional
vehicles on days with long-range trips
90 km effective el. range

## Slide 9: Total Cost for vehicle Users (TCU)
fleet type | energy cost | insurance premiums | vehicle subst. cost
car rental | user | user | -
commercial | owner | owner | -
company car | user | owner | user
private ownership | owner | owner | owner
Cost distribution by fleet type
Benefit in kind (BIK)
BIK tax total | DE | AT | NL | ES | UK
Gasoline | 6,100 € | 6,700 € | 6,600 € | 2,400 € | 7,600 €
Diesel | 7,400 € | 7,900 € | 6,800 € | 2,100 € | 8,100 €
BEV | 10,500 € | 0 € | 1,800 € | 2,900 € | 4,200 €
Company cars only
no savings in DE & ES
good savings in AT & NL
Example: C-segment

## Slide 10: Include non-monetary aspects – vehicle utility
 | TCO | Total cost for user | Acceleration | CO2 emissions
 | 1 | 1 | 468 €/s | 213 €/t
 | TCO | Total cost for user | Acceleration | CO2 emissions
 | 1 | 1 | 468 €/s | 213 €/t
Willingness-to-pay coefficients1
Combine
  TCO
  TCU
  well-to-wheel CO2 emissions
  acceleration time [0-100 km/h] (driving dynamics)
Utility of vehicle
  willingness to pay
  inverse of cost summation
  set to 100% for best conventional vehicle of same size
1Redelbach, Martin „Entwicklung eines dynamischen nutzenbasierten Szenariomodells zur Simulation der zukünftigen Marktentwicklung für alternative PKW-Antriebskonzepte“, Dissertation, Universität Stuttgart, 2016.

## Slide 11
BEV utility
compared to best conventional vehicle of same size (100% utility)
green / blue – higher BEV utility
red / orange – lower BEV utility
purple boxes mark BEV business-case regions

## Slide 13: BEV utility – findings by country
Germany & Spain
  (very) low utility
  some potential in commercial fleets D-segment
  no EV potential for private ownership & company cars
the Netherlands
  high utility in corporate fleets
  good utility for private sector with annual mileage < 25.000 km/a
Austria & the UK
  high BEV potential in corporate fleets
  reasonable utility for medium-sized company cars
  low utility for private car ownership
Summary by country | DE | NL | AT | ES | UK
# BEV utility > 100 | 0 | 226 | 150 | 71 | 133

## Slide 14: BEV utility – further findings
high BEV potential
  medium-sized cars
  light commercial vehicles
Summary by vehicle size | A | B | C | D | E | N1
# BEV utility > 100 | 25 | 20 | 78 | 90 | 17 | 145
Summary by fleet type | car rental | commercial | company car | private
# BEV utility > 100 | 46 | 145 | 54 | 10
high BEV potential
  commercial fleets
low BEV potential
    private ownership

## Slide 15: Conclusions
DE: 5000€ additional incentives needed for comparable BEV TCO
best BEV utility for
  medium-sized cars & light commercial vehicles
  commercial fleets
worst BEV utility for
  private ownership
  mini cars & large cars
CO2 emissions + acceleration do not turn the balance in favour of BEVs
Outlook
country- & fleet-type specific utility
include PEV-promoting measures
  priority lanes
  priority parking
  entry restrictions

## Slide 16: The project Incentives for Cleaner Vehicles in Urban Europe (I-CVUE)
http://dsm.icvue.eu
http://icvue.eu
Partners
Co-funded by the Intelligent Energy Europe Programme of the European Union.