## Slide 1: Injection seeded ns-pulsed Nd:YAG laser at 1116 nm for Fe-Lidar
Alexander Fischer1, Peter Mahnke1, Daniel Sauder1, Matthias Damm1, Hans Christian Büdenbender2 , Jochen Speiser1
1DLR Stuttgart Institute for Technical Physics
2DLR Oberpfaffenhofen Institute for Atmospherical Physics

## Slide 2: Motivation
Alima: Airborne Lidar for studying the
middle atmosphere
Cooperation with DLR Oberpfaffenhofen PA-LID
Iron in the upper atmosphere (50-100 km)
Fluorescence line of 372 nm suitable for
resonance Lidar
Analysis of the line gives information about
air velocity, temperature, gravity waves
Goal: compact, airborne
system
Gelbwachs J., Appl. Opt. 33, 7151 (1994)
Gardner et al, Geophys. Res. Lett. 27, 1199 (2001)
Chu et al, Appl. Opt. 41, 4400 (2002)
Kaifler et al. ;New Lidar Systems at the German Aerospace Center, LPMR 2015

## Slide 3: Generation of 372 nm: existing system
744 nm
Alexandrite laser
single frequency
2w
100 mJ
~60 ns
34 Hz
3 W
372 nm
Chu et al., Appl. Opt. 21, 4400 (2002)
developed by the NCAR
Disadvantage: small emission cross section, needs heating
strong pumping source needed

## Slide 4: Generation of 372 nm: OPO
1064 nm
single frequency Nd:YAG
1 J, 100 Hz, 10 ns
commercially available
3w
2w
2w
OPO
1116 nm
532 nm
558 nm
372 nm
>50 mJ
disadvantages: not very efficient
danger of damage of optics due to high pulse energies

## Slide 5: Generation of 372 nm: resonator at 1116 nm
1116 nm
single frequency
>15 mJ, 100 Hz, <100 ns
amplifier system
>150 mJ
3w
2w
372 nm, >50 mJ
can be realized very compact
avoids very high pulse energies
small cooling system required

## Slide 6: Nd:YAG laser line at 1116 nm
emission cross sections:
s1064 = 2,8*10-19 cm²
s1116 = 0,42*10-19 cm²
challenges with 1116 nm:
~7 times lower amplification than with 1064 nm
supression of 1064 nm
Alexandrite s744 = 0,07*10-19 cm² (295 K)
and 0,30*10-19 cm² (463 K)
Marling, IEEE J. Quant. Electron, 14, 56 (1978)
Wang et al.; Appl. Phys B (2011) 104:45–52
Huan et al.; Chin. Phys. B Vol. 21, No. 10 (2012) 104208
Zhang et al.; CHIN. PHYS. LETT. Vol. 30, No. 10 (2013) 104202

## Slide 7: Realisation of the resonator
end mirror
Pockels cell
l/4 plate
l/4 plate
pump chamber
with Nd:YAG crystal
end mirror
etalon
TFP
seed laser
diode laser @ 1116 nm
cw, 5 mW, single frequency
side pumped setup
injection seeded
resonator length ~110 cm
pump duration 300 µs @ 100 Hz
to experiment/
frequency conversion

## Slide 8: Injection Seeding
end mirror
Pockels cell
l/4 plate
l/4 plate
pump chamber
with Nd:YAG crystal
end mirror
etalon
TFP
seed laser
Need for stabilization of the resonator length
to get proper seeding
no stabilization
(bad parameters)
(2 modes)
single frequency

## Slide 9: Feedback-looped Stabilzation
l/4 plate
l/4 plate
pump chamber
with Nd:YAG crystal
end mirror
with piezo
TFP
seed laser
photodiode
Build-up-time
feedback control
Folie mit vorher kombinieren

## Slide 10: Output power and beam quality
M² ~ 1,1
maximum pulse energy ~14.3 mJ @ 1116 nm
4.9 mJ @ 372 nm (max. efficiency 35%)
output coupling ~10%
pulse length 80 ns

## Slide 11: Further Work
implementation of a end pumped resonator